## Slide 1
Event Loop
Handle Events, Send Messages, Handle Error, Shutdown Application
Top Level IA GUI Loop
Receive Messages, Update GUI, Handle Error, Shutdown
Camera HW Loop
Initialize, Check/Receive Message, Perform Action, Send Data, Handle Error, Shutdown
Camera Snapshot GUI Loop
Receive Messages, Update GUI, Handle Error, Shutdown
Force Calibration GUI Loop
Receive Messages, Update GUI, Handle Error, Shutdown
IA Test GUI Loop
Receive Messages, Update GUI, Handle Error, Shutdown
Test Equipment GUI Loop
Receive Messages, Update GUI, Handle Error, Shutdown
Camera GUI Loop
Receive Messages, Update GUI, Handle Error, Shutdown
Main Handler Loop
Receive Messages, Display Messages, Interface with Files, Handle Error, Shutdown
Force Sensor HW Loop
Initialize, Check/Receive Message, Perform Action, Send Data, Handle Error, Shutdown
LED Loop
Initialize, Receive Message, Perform Action, Handle Error, Shutdown
Servo Loop
Initialize, Receive Message, Perform Action, Handle Error, Shutdown

## Slide 2
Top Level IA GUI Loop
Update camera framerate
Update current status
Update start time
Update end time
Update calibration array
Clear calibration array
Update calibration results
Update diameter chart
Update LED
Camera Snapshot GUI Loop
Update image
Force Calibration GUI Loop
Update force chart
Plot calibration results
IA Test GUI Loop
Update diameter chart
Update force/setpoint
Clear charts
Test Equipment GUI Loop
Update force chart
Send servo position
Camera GUI Loop
Update image
Servo Loop
Update servo parameters
Update servo position
Color Code – Interfaces with…
LED
Force Sensor
Camera
Servo
Event
Controller
File Interface
LED HW Loop
Update LED parameters
Update LED switch
Send last switch state
Camera HW Loop
Update cam parameters
Read picture from camera
Send picture
Send diameter
Force Sensor HW Loop
Update DAQ parameters
Read force value
Send force value
Controller Loop
Run inflation test
  Get time
  Read force value
  Read diameter
  Decide action
  Send servo position
  Send LED state
  Save test data
Calibrate force sensor
  Read force value
  Calculate calibration
  Save calibration
Select camera calibration
Control Loop states
Event Loop
Update dynamic Tabs
Update subpanel selection
Send user action